## Slide 1: Laboratory 2 – Hardware qubit gates 058171 - Quantum Circuits and Devices
Piergiulio Mannocci

## Slide 2: Contents
Time-continuous qubit simulation
Pulse-level qubit simulation
Rabi pulse calibration
Detuning
Recap and conclusions

## Slide 3: Contents
Time-continuous qubit simulation
Pulse-level qubit simulation
Rabi pulse calibration
Detuning
Recap and conclusions

## Slide 4: Qiskit Dynamics
Qiskit Dynamics (QD) is an extension of the Qiskit framework enabling time-domain simulation of quantum systems
In QD, quantum systems are identified by Solver objects:
sobj = Solver(static_hamiltonian, hamiltonian_operators)
static_hamiltonian encodes e.g. static magnetic fields inducing Larmor precession
hamiltonian_operators encodes time-varying components, e.g. resonant fields
Example: two-level system with constant drive @ 4.95 GHz, and resonant drive with 20 MHz strength
sobj = Solver( static_hamiltonian=0.5*4.95e9*Operator.from_label('Z'), hamiltonian_operators=20e6*Operator.from_label('X'))

## Slide 5: Qubit control system

## Slide 6: Signal class
Driving signals are represented by objects of the Signal class
sig = Signal(envelope, carrier_freq)
Example: full-amplitude, constant-envelope 12.5 ns pulse followed by 12.5 ns idle (zero-amplitude) @ 4.95 GHz
envfunc = lambda t: 1.*(t <= 12.5e-9) + 0.*(t > 12.5e-9)
sig = Signal(envelope=envfunc,carrier_freq=4.95e9)
signal.draw(0,25e-9,10000)
envelope signal envelope (constant or a lambda function)
carrier_freq local oscillator frequency

## Slide 7: Time-domain simulation
The action of a Signal on the quantum system can be simulated using the .solve() method:
sol = sobj.solve(t_span, y0, signals, teval)
t_span start and end time for the quantum system simulation (nparray)
y0 initial state of the quantum system (Statevector)
signals driving signals applied to the quantum system (Signal objects)
teval time-points to evaluate during simulation (nparray)
Example: simulation from t = 0 to t = 18.75 ns of the 12.5 ns full-amplitude pulse
        sol = sobj.solve( t_span=[0,18.75e-9],
        y0=Statevector.from_label('0'),
        signals=[sig],
        teval=np.linspace(0,18.75e-9,20000))

## Slide 8: Simulation results
Pulse corresponds to a rotation around :
Expectation value for projection on is 0 (same probability of measuring +/- 1)
Larmor precession traceable in oscillations of and

## Slide 9: Rotating frame
To improve the performance (speed and accuracy) of simulations, a rotating frame can be provided:
sobj = Solver( static_hamiltonian=0.5*4.95e9*Operator.from_label('Z'), hamiltonian_operators=20e6*Operator.from_label('X'),
rotating_frame=0.5*4.95e9*Operator.from_label('Z'))
Calling sobj.solve(…) now returns:

## Slide 10: Driving phase
Driving phase can be simulated by using a complex envelope amplitude
Example: full-amplitude, in-quadrature 12.5 ns pulse followed by 6.25 ns idle (zero-amplitude) @ 4.95 GHz
envfunc = lambda t: 1j.*(t <= 12.5e-9) + 0.*(t > 12.5e-9)
sig = Signal(envelope=envfunc,carrier_freq=4.95e9)

## Slide 11: Y1/2 rotation simulation

## Slide 12: Multiple pulses
More complex envelope functions allow simulations of multiple pulses and idle times
Example: 12.5ns full-amplitude in-phase pulse, 10ns idle, 12.5 ns full-amplitude in-phase pulse (X1/2X1/2)
envfunc = lambda t: 1. * ( ( t <= 12.5e-9) |
( (t >= 22.5e-9) & (t <= 35e-9) )
);

## Slide 13: X1/2X1/2 rotation simulation

## Slide 14
Hands-on time!
Exercise 1

## Slide 15: X1/4Y1/4 rotation result

## Slide 16: X1/4Y1/4 rotation in rotating frame

## Slide 17: Contents
Time-continuous qubit simulation
Pulse-level qubit simulation
Rabi pulse calibration
Detuning
Recap and conclusions

## Slide 18: Qiskit Pulse
Gate-level simulation
Operator
QuantumCircuit
Pulse-level simulation
Pulse
Schedule
Signal-level simulation
Signal
Solver
Hardware closeness
Abstraction
Pulse-level simulation provides intermediate simulation between gate-level and signal-level
Pulse objects represent a generic interaction between the driving field and the qubit state

## Slide 19: Pulse schedules
Pulse Schedules are collections of pulses representing a sequence of pulses
Pulse durations are measured in dt units, corresponding to the time-resolution of the AWG system
Example: -phase shift + -rotation (y), idling, --phase shift + -rotation (x)
with pulse.build(name="test_sched") as sxp:
with pulse.align_sequential():
pulse.shift_phase(np.pi/2, pulse.DriveChannel(0))
pulse.play(pulse.library.Constant(dgate,1), pulse.DriveChannel(0))
pulse.delay(didle,pulse.DriveChannel(0))
pulse.shift_phase(-np.pi/2, pulse.DriveChannel(0))
pulse.play(pulse.library.Constant(dgate,1), pulse.DriveChannel(0))
pulse.acquire(duration=1, qubit_or_channel=0, register=pulse.MemorySlot(0))

## Slide 20: Pulse to Signal conversion
Schedules can be converted back to Signal objects using the InstructionToSignals function of the qiskit_dynamics.pulse module
converter = InstructionToSignals(dt, carriers={"d0": omega})
signal = converter.get_signals(sxp);
signal = signal[0];

## Slide 21: Pulse-compatible Solver object
Some additional parameters are needed when instantiating the Solver object to work with Pulse Schedules:
      solver = Solver( static_hamiltonian=hdrift,
      hamiltonian_operators=[hdrive],
      hamiltonian_channels=["d0"],
      rotating_frame=hdrift, channel_carrier_freqs={"d0":omega/2/np.pi},
      dt=dt);
hamiltonian_channels and channel_carrier_freqs represent the physical driving channels
dt is the time-resolution of the AWG system, used for inner Pulse to Signal conversion

## Slide 22: Signal-level simulation of Pulse Schedules
Pulse Schedules are now compatible with Solver instances:
      sol = solver.solve(t_span=[0,tend], y0=y0, signals=sxp, t_eval=t_eval)

## Slide 23: Pulse-level simulation
Pulse Schedules can also be run in a Backend, similar to gate-level simulation
The DynamicsBackend objects is attached to an underlying Solver object:
      backend = DynamicsBackend( solver=solver,
      subsystem_dims=[2]);
Pulse Schedules are executed on the target Backend by calling the .run() method, returning a Result:
job = backend.run([sxp], shots=1000, meas_return="single")
result = job.result()
plot_histogram(result.get_counts())

## Slide 24: Building Schedules from QuantumCircuits
Pulse Schedules can be generated also from a given QuantumCircuit and hardware specifications using the build_schedule function.
Before building the pulse schedule, circuits need to be transpiled so to use only operations available in the hardware:
service = QiskitRuntimeService(channel='ibm_quantum')
backend2 = service.least_busy();
transpiled_circ = transpile(circ, backend2)
schedule = build_schedule(transpiled_circ, backend2)

## Slide 25: Contents
Time-continuous qubit simulation
Pulse-level qubit simulation
Rabi pulse calibration
Drive frequency calibration
Recap and conclusions

## Slide 26: Pulse calibration and parametric Schedules
In real hardware, a limited set of pulses (gates), forming a universal basis for circuit transpilation, is pre-calibrated by testing different combinations of amplitude/pulse width
Owing to the limited time-resolution of AWG systems, pulse-widths are typically chosen to be an integer numer of time-steps, and the driving field amplitude is instead used to change the effective driving frequency
Parametric Pulse Schedules are typically defined for this task:
drive_amp = Parameter('drive_amp');
with pulse.build() as rabi_sched:
with pulse.align_sequential():
pulse.play(pulse.Constant(duration,drive_amp,name="RabiP"),pulse.DriveChannel(0));
pulse.acquire(1,0,pulse.MemorySlot(0));
rabi_scds = [rabi_sched.assign_parameters({drive_amp: a}, inplace=False) for a in drive_amps]

## Slide 27: -pulse amplitude estimation
Upon running the schedules, we obtain a curve representing the probability of measuring the |1> state after application of the Pulse with corresponding amplitude:
We can fit the curve with a cosinusoidal function:
The -pulse will be given by the amplitude corresponding to half of the fitted drive period D:
drive_period = fit_params[2]
pi_amp = abs(drive_period / 2)
The calibrate_rabi() helper is provided in the notebook, returning amplitudes for and pulses on a given setup

## Slide 28
Hands-on time!
Exercise 2

## Slide 29: Hadamard pulse simulation

## Slide 30: Contents
Time-continuous qubit simulation
Pulse-level qubit simulation
Rabi pulse calibration
Detuning
Recap and conclusions

## Slide 31: Detuning
Up to here, we have considered the resonant drive to be perfectly matched to the qubit frequency
To simulate the impact of imperfect matching between the driving field and qubit, we can specify a rotating_frame different from the static_hamiltonian
Example: -y, -x with 5 MHz drive/qubit mismatch

## Slide 32: Contents
Time-continuous qubit simulation
Pulse-level qubit simulation
Rabi pulse calibration
Detuning
Recap and conclusions

## Slide 33: Recap
Qiskit Dynamics allows time-continuous simulation of qubits and quantum systems
Signal-level simulation provides insight into hardware-level manipulation of qubits
Pulse-level simulation enables intermediate abstraction between gate-level and signal-level
Pulse calibration is a fundamental first step for quantum systems
Nonidealities such as detuning require more complex calibration techniques

## Slide 34: What's next?
Real quantum processors are plagued by nonidealities that affect computation results
How can we characterize these nonidealities and fine-tune our hardware implementations?
  → topic of Laboratory 3: Quantum system characterization & fine-tuning